## Slide 1
Scalar Kalman Filter

## Slide 2
Scalar Kalman filter: symbols and sequence
Each variable contains one number because the state is a single weight
What each symbol contains
x̂
Current estimate
kg, example: 8 kg
z
New measurement
kg, example: 12 kg
P
Uncertainty of x̂
kg², smaller P means higher confidence
R
Uncertainty of z
kg², smaller R means a more reliable reading
Q
Possible real change
kg², Q = 0 for constant weight
K
Measurement trust
No unit, near 1 trusts z more
Calculation for each new measurement
1
Predict
x̂⁻ = previous x̂ P⁻ = previous P + Q
↓
2
Compare
y = z − x̂⁻
↓
3
Choose trust
K = P⁻ / (P⁻ + R)
↓
4
Update
x̂ = x̂⁻ + Ky P = (1 − K)P⁻
Superscript ⁻ means the prediction before using the new measurement

## Slide 3
Scalar worked update: measurement 2
Previous estimate: x̂₁ = 8 kg, P₁ = 4 kg² New reading: z₂ = 12 kg, R₂ = 1 kg² Q = 0
1
Prediction
x̂₂⁻ = x̂₁ = 8 kg
P₂⁻ = P₁ + Q = 4 kg²
2
Innovation
y₂ = z₂ − x̂₂⁻
y₂ = 12 − 8 = 4 kg
3
Kalman gain
K₂ = P₂⁻ / (P₂⁻ + R₂)
K₂ = 4 / (4 + 1) = 0.8
4
Updated estimate
x̂₂ = x̂₂⁻ + K₂y₂
x̂₂ = 8 + 0.8(4) = 11.2 kg
5
Updated uncertainty
P₂ = (1 − K₂)P₂⁻
P₂ = (1 − 0.8)(4) = 0.8 kg²
What K = 0.8 means
The update uses 80% of the 4 kg innovation.
The estimate moves toward the reliable measurement.
Result
x̂₂ = 11.2 kg
P₂ = 0.8 kg²
The measurement improves the estimate and reduces its uncertainty.

## Slide 4
Two-Dimensional Kalman Filter

## Slide 5
Two-dimensional Kalman filter: symbols and sequence
The state contains two values: x-position and y-position
What each symbol contains
x̂
Current estimate
2×1 vector [x-position; y-position]
z
New measurement
2×1 measured position vector
P
Uncertainty of x̂
2×2 estimate covariance matrix
R
Uncertainty of z
2×2 measurement covariance matrix
Q
Possible real change
2×2 process covariance matrix
K
Measurement trust
2×2 Kalman gain matrix
Calculation for each new measurement
1
Predict
x̂⁻ = previous x̂ P⁻ = previous P + Q
↓
2
Compare
y = z − x̂⁻
↓
3
Choose trust
K = P⁻ / (P⁻ + R)
↓
4
Update
x̂ = x̂⁻ + Ky P = (I − K)P⁻
This example uses diagonal covariance matrices, so x and y update separately.

## Slide 6
Two-dimensional worked update: measurement 2
Previous estimate: x̂₁ = [8; 6] m New reading: z₂ = [11; 4.5] m Q = 0
1
Prediction
x̂₂⁻ = [8; 6] m
P₂⁻ = [4 0; 0 1] m²
2
Innovation
y₂ = z₂ − x̂₂⁻
y₂ = [3; −1.5] m
3
Kalman gain
K₂ = P₂⁻ / (P₂⁻ + R₂)
K₂ = [0.8 0; 0 0.2]
4
Updated estimate
x̂₂ = x̂₂⁻ + K₂y₂
x̂₂ = [10.4; 5.7] m
5
Updated uncertainty
P₂ = (I − K₂)P₂⁻
P₂ = [0.8 0; 0 0.8] m²
Two different gains
Kx = 0.8 trusts the new x measurement strongly.
Ky = 0.2 keeps y closer to its prediction.
Result
x̂₂ = [10.4; 5.7] m
P₂ = diag(0.8, 0.8) m²
The matrix calculation applies the same scalar idea to two state values.